## Slide 1
Design and Configuration of Automated Production Systems using Virtual Environments
Group
Yuhang Jiang
Saad Raza Hussain Shafi
June 11, 2024
Topic Model 4

## Slide 2
Robot Control Part
How Do Robots Perform on Conveyors?

## Slide 3
PL1StateMacheine.java (R1)
Assign variant to box A in the order of 2V1, 1V2, and 2V3, then take B and C from conveyor B and C respectively to assemble V1 (ABB), V2 (ABC), and V3 (ACC).
PL1StateMacheine1.java (R2)
Perform welding work for V1, V2, and V3.
PL1StateMacheine.java (R3)
Perform product sorting, placing V1 and V2 on conveyor belt D and placing V3 on conveyor belt E.
Robot Control Part

## Slide 4
PL1StateMacheine.java (R1)
Three sensors
cA1Sen: Stop the box A, trigger R1 to get B/C
cBSen: Stop the box B, tell R1 B is ready.
cCSen: Stop the box C, tell R1 B is ready.
Robot Control Part
cCSen
cBSen
cA1Sen

## Slide 5
PL1StateMacheine.java (R1)
Challenge:
How to prevent a robot from overlapping with the first box when placing the second box?
Solution:
‘VxHeight’ is a boolean variable used to control the height adjustment of the robot when placing the second box. Specifically, V1Height acts as a flag indicating whether a height adjustment is necessary to avoid overlap in V1.
Robot Control Part

## Slide 6
Robot Control Part

## Slide 7
PL1StateMacheine1.java (R2)
One sensor
cA2Sen: Stop the Vx, trigger R2 to start welding.
Robot Control Part
cA2Sen

## Slide 8
Robot Control Part
PL1StateMacheine1.java (R2)
Challenge:
How to make the welding gun move naturally along the connected edges while in motion?
Solution:
Adjust the welding gun direction only at turning points.
Don’t move. Only adjust the direction.
Don’t change the direction. Only linear move.

## Slide 9
Robot Control Part

## Slide 10
PL1StateMacheine2.java (R3)
One sensor
cA3Sen: Stop the Vx, trigger R3 to sort.
Robot Control Part
cA3Sen

## Slide 11
Data Visualization Part
Production Stats

## Slide 12
Data Visualization Part
Which and How many by Variants?
How much parts are being scraped?
How much parts are being produced?

## Slide 13
Data Visualization Part
Which and How many by Variants?
How much parts are being scraped?
How much parts are being produced?
By counting the number of Parts A, B, C using Photocells on Conveyor A, B, and C

## Slide 14
Data Visualization Part
Which and How many by Variants?
How much parts are being scraped?
Counting the Parts being scrapped in 10minutes using Photocells
How much parts are being produced?
By counting the number of Parts A, B, C using Photocells on Conveyor A, B, and C

## Slide 15
Data Visualization Part
Which and How many by Variants?
Counting the products(welded boxes) using RFIDs and “variant”
How much parts are being scraped?
Counting the Parts being scrapped in 10minutes using Photocells
How much parts are being produced?
By counting the number of Parts A, B, C using Photocells on Conveyor A, B, and C

## Slide 16
Data Visualization Part
What’s Happening on Conveyors?

## Slide 17
Data Visualization Part
Which Variant is on the Main Conveyor?
How fast Welding is being done?
How fast assembly is being done?
Are the Conveyor B and C crowded?

## Slide 18
Data Visualization Part
Which Variant is on the Main Conveyor?
By using RFID to detect the current variant going for welding
How fast Welding is being done?
By counting the number of welded Parts in 10 min using Photocells after R1
How fast assembly is being done?
By counting the number of assembled Parts in 10 min using Photocells after R1
Are the Conveyor B and C crowded?
By using Distance Sensor to detect the crowdedness on these Conveyors

## Slide 19
Data Visualization Part
Which Variant is on the Main Conveyor?
By using RFID to detect the current variant going for welding
How fast Welding is being done?
By counting the number of welded Parts in 10 min using Photocells after R1
How fast assembly is being done?
By counting the number of assembled Parts in 10 min using Photocells after R1
Are the Conveyor B and C crowded?
By using Distance Sensor to detect the crowdedness on these Conveyors

## Slide 20
Data Visualization Part
Which Variant is on the Main Conveyor?
By using RFID to detect the current variant going for welding
How fast Welding is being done?
By counting the number of welded Parts in 10 min using Photocells after R1
How fast assembly is being done?
By counting the number of assembled Parts in 10 min using Photocells after R1
Are the Conveyor B and C crowded?
By using Distance Sensor to detect the crowdedness on these Conveyors

## Slide 21
Data Visualization Part
Dashboard

## Slide 22
Data Visualization Part

## Slide 23
Data Visualization Part

## Slide 24
Data Visualization Part

## Slide 25
Data Visualization Part

## Slide 26
Which Variant is on the Main Conveyor?
By using RFID to detect the current variant going for welding
How fast Welding is being done?
By counting the number of welded Parts in 10 min using Photocells after R1
How fast assembly is being done?
By counting the number of assembled Parts in 10 min using Photocells after R1
Total Variants Produced in the last 10 minutes?
By using Distance Sensor to detect the crowdedness on these Conveyors
Data Visualization Part

## Slide 27
Data Visualization Part

## Slide 28
Data Visualization Part
Data Visualization Part

## Slide 29
How much parts are being scraped?
Counting the Parts being scrapped in 10minutes using Photocells
Which and How many by Variants?
Counting the products(welded boxes) using RFIDs and “variant”
Data Visualization Part

## Slide 30
Data Visualization Part

## Slide 31
Thank you for your attention.